## Slide 1
NXT1 and NXT2 park at the end of the performance, simultaneously.
1. ARCHITECT PERFORMANCE
RESCUE MISSION
5
3
BRIDGE CROSSING
4
LINE TRACKING
II. Land on rover
III. Balance on moving rover
3
6
1
LINE TRACKING
5
NXT1 tips seesaw
NXT1 & NXT2 on seesaw
NXT1 & NXT2 tip seesaw
NXT1 leaves seesaw
NXT2 rescued
NXT1 on seesaw
VI. End of bridge cross
SETUP CONFIGURATION
ROVER
Master
Slave
4
FINALE
6
2
START PERFORMANCE
V. Move down ramp
I. Go on ramp
I. Start from Outer Course
2
NXT1 starts from the outer course. It will perform two short-cuts through the basic stage.
I. NXT1
NXT1 enters performance stage through outer line and moves towards the up-ramp.
II. NXT2
NXT2 parked with tail down waiting for NXT1 to rescue.
NXT1 and NXT2 line-track towards corner of the stage.
I. Synchronized Line-Track:
NXT2
I. Up & Down Ramp
II. Seesaw
III. Communications
NXT1
Slave
Navigation Line
Length:
Height:
Steepness:
Down Ramp: 5% steep
Seesaw: 5% steep
NXT2
Slave
II-Shortcut1. Outer to Inner Track
NXT1 cuts across to outer track and realigns line-track using inner-track line.
II. Synchronized Parking:
NXT1
1
II-Shortcut2. Cut through Outer track
NXT1 cuts through inner and outer track then tracks using inner-track.
Communication Station
(Raspberry Pi)
Performance Stage

## Slide 2
2. REQUIREMENTS ANALYSIS
1: REQUIREMENTS ANALYSIS
3:. NON-FUNCTIONAL REQUIREMENTS
<<Requirement>>
Successful Architect Performance
<<Requirement>>
Successful
BRIDGE CROSSING
<<Requirement>>
Sufficient navigation track design
<<Requirement>>
Minimize time to finish basic stage.
Goal: < 30 seconds
<<Requirement>>
Excellent model documentation
<< Requirement>
Complete performance within 2 mins
<<Requirement>>
Successful Basic Stage
<<Requirement>>
Successful Performance Stage
<< Requirement>>
Not disqualify
<<Requirement>>
Successful
RESCUE MISSION
<<Requirement>>
Successful
LINE-TRACKING
<<Requirement>>
Efficient Development Process
<<Requirement>>
Efficient Development Process
Use of MATLAB & Simulink
<<Requirement>>
Configuration Management
<<Requirement>>
Use Rapid-Prototyping process
Use of Simulink Target Hardware Support Package
<<Requirement>>
Parallel Development Process
Step Detection
Step-off Ramp Detection
Blind run for shortcut
Distance Sensor detection
<<Requirement>>
Rover to move NXT1 from one ramp to the other ramp
Rover drive control
<<Requirement>>
Rover must move straight from one ramp to other
<<Requirement>>
NXT1 and NXT2 must line-track in synchronously.
<<Requirement>>
NXT1 and NXT2 must perform parking synchronously.
Build custom track for navigation
<<Requirement>>
Use Model-Based Design process
Use of SVN
Use of Simulink Projects
Bluetooth communication
Speed Control
<<Requirement>>
Efficient Development Structure
<<Requirement>>
Efficient Verification Process
<<Requirement>
Use a tool to log test signals for verification
Develop and use Bluetooth data logging tool
2: FUNCTIONAL REQUIREMENTS
<<Requirement>>
Successful
FINALE PERFORMANCE
Ambient Light Elimination
Current Angle Estimation
Switching PID Parameters
<<Requirement>>
Efficient & reliable LINE-TRACKING algorithm
<<Requirement>>
NXT1 and NXT2 must communicate with each other
<<Requirement>>
Finish architect performance in
1 min and 30 seconds
<<Requirement>>
NXT1 shall go up and down the ramp.
<<Requirement>>
NXT1 to tip over the seesaw and rescue NXT2
<<Requirement>>
NXT shall line track while on a ramp.
<<Requirement>>
NXT1 and Rover must communicate with each other
Element Technologies
6
PG.5
5.1
5.1.A
5.2
5.4
7.1
7.1
5.1.B
5.1
Please refer to the following sections for details.
The following is high-level requirement for the architect performance based on the concept design stage.
Requirements are further divided into functional and non-functional requirements.
3.5
3.3
3.6

## Slide 3
1: DEVELOPMENT ENVIRONMENT
3: PROJECT MANAGEMENT
5: RAPID PROTOTYPING
2: MODEL-BASED DESIGN
3. DEVELOPMENT PROCESS AND TOOLS
6: MODEL TEST AND VERIFICATION
We use the MATLAB and Simulink environment throughout the entire development process.
These tools facilitate:
Requirements linking
System-level design
  Model architecture
  Configuration management
  Data management
Algorithm Design
Rapid Prototyping
Verification and Validation
Accelerating the pace of engineering and science.
We can automatically generate code from Simulink models and build them onto low-cost embedded systems using Simulink Support Packages for Target Hardware.
This enables us to reuse simulation algorithms and automatically build them on the performance embedded devices:
LEGO Mindstorms NXT
Arduino Mega 2560
Raspberry Pi
4: SIMULINK MODEL MANAGEMENT
We promote concurrent model development by using Subversion (SVN) for source control. Simulink Projects is used to integrate SVN into the MATLAB environment.
Models are represented by using Simulink block diagrams.
Stateflow for modeling complex control logic using flow graphs and state machines,
Simulink libraries and model reference help with concurrent development in separate files.
Data dictionaries and model variants to store, modify and switch model configurations.
Bluetooth data logging:
Custom tool to collect sensor, state and logic data while running a model on embedded hardware.
External mode:
Visualize data
Tune parameters
while a model is running on embedded hardware.
Requirements can be linked to Simulink models using the Simulink Verification and Validation product.
The Model-based Design (MBD) approach is centered around a model of a real system.
All design changes can happen at the model level. All associated tasks can be easily updated with the changes to the model.
We can create a physical model of the LEGO Mindstorms NXT and test our control algorithm design in simulation.
We can perform Component-level design of control algorithms and test them by creating artificial inputs in Simulink.
Finally, we can automatically generate code from these models onto embedded systems and verify the algorithm behavior.
Then, we can perform System-level integration to test the performance of algorithms in the entire system.
Simulink Model
C Code
SYS1
SYS2
SYS3
SYS0
SYS1
C Code
Simulink Library:
Contains driver blocks
MATLAB files
Simulink models
Requirements
document
Model
Link
Select signals for logging
View and compare runs in Simulation Data Inspector
Embedded target communicates with host computer using TCP-IP over USB.
Model
(Host PC)
Hardware
Tune parameters
Receive run-time data
Run-time Display
Main model
Library models
(dependencies)

## Slide 4
4. NXT MODEL ARCHITECTURE
Tasks
Each task is developed independently and placed in a separate project folder under source control
1: MODEL OVERVIEW
2: HARDWARE
4: CONTROLLER
Robot sensors and actuators are accessed through the Simulink Support Package for LEGO Mindstorms NXT.
Actuators
Motor PWM
LCD debug display
Bluetooth send
Sensors
Motor encoders
Light/Gyro/Ultrasonic
Buttons
Battery
Bluetooth receive
Normal Operation
task complete
Do Task
entry:
start task
exit: next task
E-Stop
entry: stop moving
Controller
C. Task Management:
Tasks are executed using a Track Mode List.
This is a vector of OperationModeEnum enumerated data type.
Each task outputs its status. This is done with an enumeration of type OperationModeStatusEnum.
B. Task Component:
Each task must interface with the main controller using the following specification.
A. Control Logic:
Unless there is an emergency, the controller will execute all defined tasks sequentially.
task aborted or robot falls
push
button
Task
interface
Outputs
Motor PWM
Bluetooth command
Task status
Sensor initialize flags
Debug flags (for LCD)
Task
Component
Example Track Mode List: 1. LIGHT_CALIBRATION_UP 2. GYRO_CALIBRATION
start
start
4. SEE_SAW
5. PARKING
If the final task is marked complete, the robot will loop back to the first task.
Start
entry: start moving
Status = IN_PROGRESS
Finish
entry: stop moving
Status = COMPLETED
Failure
entry: stop moving Status = ABORTED
end of line
lost line
To next task
To E-Stop
start
3. LINE_TRACKING
Hardware
I/O
State
Estimation
Controller
et_robocon.slx
Line Track
Balance
Bridge
Crossing
Rescue Mission
…
Simulink® model built on LEGO Mindstorms NXT
Utilities in controller
Inputs
States
Sensors
Simulink Model
Generate C Code
Create RXE File
Automatic code
generation
Automatic build and download through Cygwin
GNU ARM
toolkit
Generated code translates Simulink driver blocks into nxtOSEK functions
3: STATE ESTIMATION
Side view
Top view
Converts sensor values into states. States used for balancing and line tracking.
Turning angle and Steer angle :
= Wheel radius
= Distance between wheels
All state estimation integrals are reset to zero using initialize flags from the controller.
GYRO READINGS
= Robot tilt rate
Read Gyro
Read
Encoders
Filter and compute
Compute
Compute other states
All states:
Tilt angle : Low pass filtered integral of gyro reading
ENCODER READINGS
= Left motor angle = Right motor angle
C
C

## Slide 5
5. CONTROL ALGORITHMS
1: LINE TRACKING
3: BALANCING
Balancer states do not perform any lateral () correction, so only 5 out of 8 states are used.
Balancing commands can be added to line tracking or proportional control.
K is a 1x5 matrix
K is defined in each task and can be changed every time step.
PWM commands lie in the range -100 to 100, and are replicated to both left and right wheels.
Select Balancer states
Full-state feedback control
Scale by battery voltage + saturate
start
end
2: PHI CONTROL
1
2
3
4
5
6
State Estimation
Poll Light Sensor
Lookup
Table
Find Track Zone
Select Control Gains
Compute Forward and Turning Speeds
bias
Control
Gains
Sensors
where
PID Control Law:
Poll Light Sensor
Read On
entry:
turn light on
read
start
Read Off
entry:
turn light off
read
Performance Stage
Filter
Values
From experimental data
Filter Light Values
Lookup Table
White
Black, Edge and White from calibration
1
0
0.5
Black
Edge
+ Bias
Bias value modified based on track zone
Balancing Algorithm
Track is divided into Zones
Consists of 2 algorithms:
Light processing
Track zone control
A: LIGHT PROCESSING
B: TRACK ZONE CONTROL
To Balancing Algorithm:
Track Zone:
Determined based on distance and angle traveled by the robot.
Forward and turning speeds are reference states in balancing controller.
Line tracking is turned off during the Zone 4 shortcut.
4: RAMP DETECTION
Phi control is used when:
There is no line
Line tracking is difficult
In case (2), phi control and line tracking are combined with a weighted average.
Get . from states
Proportional feedback control
Scale by battery voltage + saturate
start
end
= Wheel radius
= Distance between wheels
Light sensor values
Approach:
Robot is moving toward the ramp and must detect it.
Impact:
Large backwards force upon contact with ramp.
Recovery:
Need to provide a large velocity command to overcome bump and gravity.
and are large and negative, so ramp can be easily detected through these states.
DETECT!
Ramp and Seesaw have different thicknesses, so their impact conditions are determined separately.
Impact conditions are found through experiment.
Ramp Condition:
Thin material, gentle bump
for 10 consecutive time steps
Seesaw Condition:
Thick material, sharp bump
and

## Slide 6
6. COMMUNICATIONS
1: COMMUNICATIONS OVERVIEW
5: MESSAGING
3: BLUETOOTH WITH ARDUINO
2: BLUETOOTH WITH RASPBERRY PI
Raspberry Pi
(HOST)
NXT1
Rover
(Arduino Mega 2560)
4: HOST MODEL
UDP Recv
NXT1
etrobocon_host.slx
Simulink® model built on Raspberry Pi
Enable Flags
Logic
(State Machine)
Receiving is periodic
(every 0.1 s)
Sending is asynchronous (function call)
UDP Utilities
INIT()
SEND()
BYE()
INIT command:
Server creates one client for each enable flag
serialPort_client.c
serialPort_client.c
serialPort_client.c
Each client receives periodic Bluetooth messages from one robot
Convert Bluetooth message from robot to UDP message for host
UDP
UDP
Wait
Open serial ports and client processes
Send . to Robot
Close serial ports and client processes
INIT()
message
SEND()
message
BYE() message
Simulink Model
Generate C Code
Create Executable
Uses the Simulink Support Package for Raspberry Pi Hardware
Automatic code
generation
Automatic remote Linux Build: SSH over Wi-Fi
Driver blocks for Raspberry Pi used:
Communications: UDP Send, UDP Receive
Push button to start model: GPIO Read
UDP to Bluetooth conversion using serialPort_serv and serialPort_client
Simulink model etrobocon_host.slx is automatically built on Raspberry Pi.
Background process serialPort_serv loaded at startup on Raspberry Pi
Simulink Model
Generate C Code
Create HEX File
Automatic code
generation
Automatic build and download
Uses the Simulink Support Package for Arduino Hardware
gcc
avr-gcc
Driver blocks for Arduino used: Communications: Serial Send, Serial Receive Rover Control: Analog Input, Continuous Servo Write
Serial to Bluetooth conversion using Bluetooth Silver Mate hardware
Raspberry Pi is the host.
All Bluetooth communication between robots is done through the host.
Receive status messages
+
Broadcast commands
UDP Message Protocol: Raspberry Pi
NXT2
Control Switch:
A: 1 is data (SEND) 2 is control (INIT/BYE) B: Robot ID
1 = NXT1 2 = NXT2 3 = Arduino
4 = NOT USED C: Bluetooth Mailbox ID
(for data validation)
Message length (in bytes)
INIT command only:
PI: Probe Interval
(in milliseconds)
PL: Probe message length (in bytes)
EF: Enable flags (in decimal form)
1
1
1
0
Enable NXT1, NXT2 and Arduino: EF = dec(1110) = 14
ABC
Len
Message
PI
PL
EF
Bluetooth Message Protocol: NXT / Arduino
0
Mail
Message
Len
Message length (in bytes)
Bluetooth Mailbox ID
(for data validation)
Type of command
(to request reply)
No reply = 0
Sample Stateflow chart built on Raspberry Pi
Status/Command Messages:
Robots receiving messages are represented by a RobotID enumerated data type.
Status and command messages are unsigned integers (1 byte) of StatusID enumerated data type.
See the example Stateflow chart below for usage of INIT, SEND and BYE messages.
Periodic inputs over UDP
start
Each robot has an Enable Flag
0 : No communication 1 : Enable Bluetooth
serialPort_serv.c
Server sends asynchronous Bluetooth messages to each robot
Convert UDP message from host to Bluetooth message for robot
SERVER LOGIC
UDP Recv
NXT2
UDP Recv
Arduino
Push Button

## Slide 7
7. PERFORMANCE ALGORITHMS
NXT1_GO_BACK
1: BRIDGE CROSSING
2: RESCUE MISSION
1
2
3
4
5
NXT1
ROVER
HOST
ROVER_SENSED_RAMP
NXT1_GO_DOWN_RAMP
NXT1 on Seesaw
1
NXT1 tips Seesaw
2
Both robots on Seesaw
3
Robots tip Seesaw
4
NXT1 leaves Seesaw
5
NXT2 Rescued
6
Line Tracking
Go Up
Ramp
Stop Over Rover
1
2
start
start
Stand By
Go Forward
Slow Down and Stop
3
Go Down
Ramp
5
4
Side Infrared Sensor:
Rover senses when NXT1 is standing over it.
Front Infrared Sensor:
Rover senses when it approaches the down ramp.
ROVER:
SIDE INFRARED SENSOR
Ramp
Detection
Based on
distance
Wait for
message
Wait for
sensor
Wait for
sensor
To Line
Tracking
NXT1
NXT2
HOST
Line Tracking
Go Up
Seesaw
Balance
1
2
start
start
Stand By
Turn
180°
Based on
distance
Wait for
message
To Line Tracking
Ramp
Detection
Stand up on tail
Balance
Go Forward
Go Up
Seesaw
Balance
Go Back on Seesaw
Based on
distance
Wait for
message
Ramp
Detection
Leave Seesaw
Go Back on Seesaw
Based on
distance
Get off Seesaw
Based on
distance
Based on
distance
To Line Tracking
6
3
NXT1_ON_SEESAW
NXT2_STAND
NXT1_WAITING
NXT2_START
NXT2_ON_SEESAW
NXT1_LEAD
NXT2_FOLLOW
Move on Seesaw
Balance
NXT1_OFF_SEESAW
NXT2_WAIT
NXT1_TURNED
NXT2_LEAVE
Wait for
message
Wait for
message
Wait for
message
Wait for
message
4
5
Infrared sensor data is filtered with a 5 point moving average in order to avoid false positives.
FALSE
POSITIVE
OBJECT
DETECTED
ROVER DESIGN:
Analog infrared distance sensors:
ANALOG INPUT
12V DC Motors with digital controller
DIGITAL OUTPUT
Serial Bluetooth module:
SERIAL READ/WRITE